## Slide 1
COMPRESSION
AISC Manual – 16th Edition
ANSI/AISC 360-22
Developed by Scott Civjan
University of Massachusetts, Amherst
Teaching Modules for
Steel Instruction

## Slide 2
Compression Members:
  Chapter E: Compression Strength
  Chapter I: Composite Member Strength
  Part 4: Design Charts and Tables
  Chapter C: Analysis Issues

## Slide 3
Local Buckling:
  Criteria in Table B4.1
  Strength in Chapter E: Members with Slender Elements

## Slide 4
Local Buckling Criteria
Slenderness of the flange and web, l, are used as criteria to determine whether local buckling might control in the elastic or inelastic range, otherwise the global buckling criteria controls.
Criteria r are based on plate buckling theory.
For W-Shapes
FLB,  = bf /2tf rf =
WLB,  = h/tw rw =
Notes: Depends on 2 variables:1)Width to thickness ratio of flange and/or web and 2)Fy
Values are more stringent from those provided for beams, as the entire section is under full compression, and therefore less likely to provide restraint to the adjacent sections. In a W-shape beam bent about the major axis, only part of the web is in compression, and the value is minimal near the centroid, allowing the web to provide additional restraint to the flanges. Also, the web in such a beam is only partially under compression, so is much less likely to buckle than in a compressive member.

## Slide 5
 > r “slender element”
Failure by local buckling occurs.
Covered in Section E7
Many rolled W-shape sections are dimensioned such that the full global criteria controls.
Local Buckling
Notes: In general practically all W-shapes are non-slender as compression members, so this is covered as an advanced topic only.
May control if high Fy, welded shapes, shapes not generally used for compression (such as angles, WT, etc.)

## Slide 6
  Chapter E:
  Compression Strength

## Slide 7
fc= 0.90 (Wc= 1.67)
Compression Strength

## Slide 8
Specification considers the following conditions:
  Flexural Buckling
  Torsional Buckling
  Flexural-Torsional Buckling
Compression Strength
Notes: Note that for W-shape and tube members, only global flexural buckling needs to be checked

## Slide 9
  Compressive Strength

## Slide 10
The following slides assume:
  Non-slender flange and web sections
  Doubly symmetric members
Compression Strength

## Slide 11
Since members are non-slender and doubly symmetric,
flexural (global) buckling is the most likely potential failure mode prior to reaching the squash load.
Buckling strength depends on the slenderness of the section, defined as Lc/r. Lc is the effective length of the member.
The nominal strength is defined as
Pn= FnAg Equation E3-1
Compression Strength
Notes: Equation E3-1 defines the strength as an effective critical stress times the gross area of the cross section.
Fcr is therefore limited to Fy, which would indicate the squash load.

## Slide 12
Fe = elastic (Euler) buckling stress, Equation E3-4
If , then Fn = 0.877Fe. Equation E3-3
This defines the “elastic” buckling limit
with a reduction factor, 0.877, times the theoretical limit.
If then, . Equation E3-2
This defines the “inelastic” buckling limit.

## Slide 13
Lc /r
Inelastic Material Effects
s
Elastic Behavior
Notes: Inelastic action reduces column strength for lower values of KL/r. The maximum possible strength is the crushing limit, where all of the cross section attains Fy. Using tangent modulus theory, we can use a reduced modulus of elasticity, Et in the Euler Buckling equation. Et is obtained from a “Stub Column” (very short section in compression) test as shown on the previous page. Alternatively, one could assume that the entire cross section continues to have a material property, E, but that all yielded portions of the cross section are no longer effective, reducing I. In other words, ET = (Ie/I)E where Ie = I of non-yielded cross section. The end result is similar, as it is the combined stiffness parameter EI that controls the buckling strength.
13

## Slide 14
Lc /r
s
Fy-Fres
Fy
Inelastic
Elastic
Inelastic Material Effects
Notes: Inelastic action reduces column strength for lower values of KL/r. The maximum possible strength is the crushing limit, where all of the cross section attains Fy. Using tangent modulus theory, we can use a reduced modulus of elasticity, Et in the Euler Buckling equation. Et is obtained from a “Stub Column” (very short section in compression) test as shown on the previous page. Alternatively, one could assume that the entire cross section continues to have a material property, E, but that all yielded portions of the cross section are no longer effective, reducing I. In other words, ET = (Ie/I)E where Ie = I of non-yielded cross section. The end result is similar, as it is the combined stiffness parameter EI that controls the buckling strength.
14

## Slide 15
Lc /r
s
Fy-Fres
Fy
Inelastic
Elastic
Inelastic Material Effects
Notes: Inelastic action reduces column strength for lower values of KL/r. The maximum possible strength is the crushing limit, where all of the cross section attains Fy. Using tangent modulus theory, we can use a reduced modulus of elasticity, Et in the Euler Buckling equation. Et is obtained from a “Stub Column” (very short section in compression) test as shown on the previous page. Alternatively, one could assume that the entire cross section continues to have a material property, E, but that all yielded portions of the cross section are no longer effective, reducing I. In other words, ET = (Ie/I)E where Ie = I of non-yielded cross section. The end result is similar, as it is the combined stiffness parameter EI that controls the buckling strength.
15

## Slide 16
Lc /r
s
Fy
Inelastic
Elastic
Inelastic Material Effects
0.44Fy
Notes: Inelastic action reduces column strength for lower values of KL/r. The maximum possible strength is the crushing limit, where all of the cross section attains Fy. Using tangent modulus theory, we can use a reduced modulus of elasticity, Et in the Euler Buckling equation. Et is obtained from a “Stub Column” (very short section in compression) test as shown on the previous page. Alternatively, one could assume that the entire cross section continues to have a material property, E, but that all yielded portions of the cross section are no longer effective, reducing I. In other words, ET = (Ie/I)E where Ie = I of non-yielded cross section. The end result is similar, as it is the combined stiffness parameter EI that controls the buckling strength.
16

## Slide 17
Design Aids
Table 4-14
fcFn as a function of Lc/r
Tables 4-1 to 4-12
fcPn as a function of Lcy
Useful for all shapes.
Larger Lc/r value controls.
Can be applied to Lcx by dividing Lcy by rx/ry.

## Slide 18
Slenderness Criteria
Notes: Note Lc/r=slenderness parameter. Lc=effective length (KL).
This criteria is mostly based on erection and shipping concerns rather than safety issues.

## Slide 19
Per Section E.2
It is recommended to provide Lc /r less than 200

## Slide 20
Alignment Chart Issues
Figures C-A-7.1 and C-A-7.2

## Slide 21
To account for inelastic column effects,
stiffness reduction factors, tb,
used to reduce EI of the columns.
Stiffness Reduction Factors
Table 4-13
Alignment Chart

## Slide 22
If beams have significant axial load,
they provide less rotational restraint.
1-Q/Qcr
Q = axial load
Qcr = axial in-plane buckling strength with K=1
Reduce rotational stiffness component (EI/L) of beams with modification,
This is also valid for “columns” at a joint (multiple stories), which carry minimal axial load compared to their strengths.
Alignment Chart

## Slide 23
To account for story buckling concept, all columns must reach their capacity to allow for story failure.
Revise K to account for story effects.
Alignment Chart
Kn2 = K factor directly from the alignment chart
Pr = Required second-order axial strength
Pstory = total vertical load supported by the story
K2 from Equation C-A-7-8