## Slide 1
Compression Member Design
Developed by Scott Civjan
University of Massachusetts, Amherst
Teaching Modules for
Steel Instruction

## Slide 2
COMPRESSION MEMBER/COLUMN:
Structural member subjected to axial load
P
P
Notes: Note that “column” is used in these slides interchangeably for “compression member”. This is not technically correct, but was adopted based on nomenclature in existing modules. Members are designed for the type of force in the member and a “column” in a structure could have compression or tension in the member depending on the load conditions. However, compression members are typically controlled by compression while the connections may require additional attention to tension loads.
If also includes flexural loads – handle as Combined Load – see Module #3
Typically vertical members of a frame, such as columns, braces, truss members

## Slide 3
INSERT PHOTOS:
Compression Members in Structures:
AISC WET Columns Slide Show
AISC Four Story Office Building
Photo Slide Shows
Structural Steel Erection Slides

## Slide 4
Strength design requirements:
Pu  Pn (Pa  Pn/Ω)ASD
Where  = 0.9 for compression
(Ω = 1.67)ASD
Notes: Note that subscript u= ultimate foREVISE FOR ASD/LRFD
Note that flexure typically controls strength design. Shear can control for shorter length “Deep Beams”
Generally design for critical condition independently, check others, revise as needed
Design is iterative.
Module will address each of these criteria separately (moment, shear, serviceability)

## Slide 5
Axial Strength
Strength Limit States:
Squash Load
Global Buckling
Local Buckling
Notes: Each of these limit states will be evaluated individually. The lowest strength will control design strength.
Define buckling is the loss of compressive load carrying capacity resulting from a change in the geometry of the member, this differs somewhat from a classical approach of defining buckling as a bifurcation point, but as we will see a true bifurcation point is generally not realized in an actual member.
Global buckling will typically limit strength. For very short “stub” columns, or fully braced sections (such as buckling restrained bracing) reaching the “squash load” can control. Local buckling can control members with slender elements (flange or web)

## Slide 6
Global Buckling
Local Flange Buckling
Local Web Buckling
Notes: Each of these failure modes will be evaluated individually. The lowest strength will control design strength.
Define buckling is the loss of compressive load carrying capacity resulting from a change in the geometry of the member, this differs somewhat from a classical approach of defining buckling as a bifurcation point, but as we will see a true bifurcation point is generally not realized in an actual member.
Global buckling will typically limit strength. For very short “stub” columns, or fully braced sections (such as buckling restrained bracing) crushing can control. Local buckling can control members with slender elements (flange or web)

## Slide 7
INSERT INFORMATION: FAILURE MODES
AISC WET Columns Slide Show
Video:
AISC: The Behavior of Columns

## Slide 8
INSERT INFORMATION: FAILURE MODES
Animations:
AISC WET: Column Buckling, Local Buckling
Demonstrations:
AISC Educator Forum:
PaperColumn_Liu.PDF, Buckle_Bracing_Civjan.PDF
Notes: Demonstrations are available on the AISC Educator Forum (educatorforum.aisc.org)
Paper Column Demo link: https://educatorforum.aisc.org/resource/asset/1452

## Slide 9
INSERT INFORMATION:
Sample AISC Tables
Table_4-1_pp16-17.PDF
Table_4-8_pp145.PDF
Table_4-9_pp157.PDF
Table_4-10_pp170.PDF
Table_4-11_pp188.PDF
Table_4-11_pp195.PDF
Table_4-13_pp227.PDF
Table_4-14_pp228-232.PDF

## Slide 10
INSERT SLIDES: COMPRESSION THEORY
Compression_Theory.ppt
INDIVIDUAL COLUMNS
Single Member Global Buckling
Slides # 2 to 35
Local Buckling
Slides # 36 to 42
Equivalent Length
Slides # 26 to 27

## Slide 11
INSERT SLIDES: COMPRESSION DESIGN
Compression_Manual.ppt
INDIVIDUAL COMPRESSION MEMBER
Global Buckling, Compact
Slides # 6 to 17
Local Buckling
Slides # 3 to 5
Slenderness
Slides # 18 to 19

## Slide 12
ALIGNMENT CHART
OR
DIRECT ANALYSIS METHODS
For Members within a Structure:
Instructor Should Decide on
Either
Alignment Chart (Slide 11-12)
Or
Direct Analysis Method (Slides 13-14)
as the primary focus of instruction and
adopt the appropriate theory and specification slides.

## Slide 13
INSERT SLIDES: COMPRESSION THEORY
Compression_Theory.ppt
MEMBER WITHIN STRUCTURE
Alignment Chart
Slides # 48 to 95
Leaner Columns:
Slides # 81 to 90
Direct Analysis Method
Slides # 97 to 98

## Slide 14
INSERT SLIDES: COMPRESSION DESIGN
Compression_Manual.ppt
Alignment Chart
Leaner Columns:
Slides # 20 to 23

## Slide 15
INSERT SLIDES: DESIGN
ADVANCEDCompression_ManualSlender.ppt
Advanced Topics
Slender Flange or Web:
Slides # 1-10