## Slide 1
COMPRESSION THEORY SLIDES
Developed by Scott Civjan
University of Massachusetts, Amherst
Teaching Modules for
Steel Instruction

## Slide 2
INDIVIDUAL COLUMN
Notes: Initially it’s easiest to describe behavior of an individual column, then introduce the role and analysis of a column within an entire structure. The full structure can be conceptualized as varying the end conditions of individual columns.

## Slide 3
Squash Load
Fully Yielded Cross Section

## Slide 4
When a short, stocky column is loaded the strength is limited by the yielding of the entire cross section.
Absence of residual stress, all fibers of cross-section yield simultaneously at P/A=Fy.
D
P=FyA
eyL0
P
P
D
L0
Notes: Crushing is often called the “squash load”, the load at which the entire cross section would yield.

## Slide 5
Results in a reduction in the effective stiffness of the cross section, but the ultimate squash load is unchanged.
Reduction in effective stiffness can influence onset of buckling.
RESIDUAL STRESSES

## Slide 6
D
P=FyA
eyL0
No Residual Stress
6
Compression Theory
With residual stresses, flange tips yield first at
P/A + residual stress = Fy
Gradually get yield of entire cross section.
Stiffness is reduced after 1st yield.
RESIDUAL STRESSES
Notes: Maximum achieved load is therefore still P=AFy, but the load deflection curve is very different, stiffness is reduced.
6

## Slide 7
With residual stresses, flange tips yield first at
P/A + residual stress = Fy
Gradually get yield of entire cross section.
Stiffness is reduced after 1st yield.
D
P=FyA
eyL0
RESIDUAL STRESSES
7
Compression Theory
P=(Fy-Fres)A
1
No Residual Stress
= Yielded
Steel
1
Notes: Maximum achieved load is therefore still P=AFy, but the load deflection curve is very different, stiffness is reduced.
7

## Slide 8
With residual stresses, flange tips yield first at
P/A + residual stress = Fy
Gradually get yield of entire cross section.
Stiffness is reduced after 1st yield.
D
P=FyA
eyL0
RESIDUAL STRESSES
8
Compression Theory
P=(Fy-Fres)A
1
= Yielded
Steel
2
No Residual Stress
1
2
Notes: Maximum achieved load is therefore still P=AFy, but the load deflection curve is very different, stiffness is reduced.
8

## Slide 9
With residual stresses, flange tips yield first at
P/A + residual stress = Fy
Gradually get yield of entire cross section.
Stiffness is reduced after 1st yield.
D
P=FyA
eyL0
RESIDUAL STRESSES
9
Compression Theory
P=(Fy-Fres)A
1
= Yielded
Steel
1
2
2
3
3
No Residual Stress
Notes: Maximum achieved load is therefore still P=AFy, but the load deflection curve is very different, stiffness is reduced.
9

## Slide 10
With residual stresses, flange tips yield first at
P/A + residual stress = Fy
Gradually get yield of entire cross section.
Stiffness is reduced after 1st yield.
D
P=FyA
eyL0
RESIDUAL STRESSES
Compression Theory
P=(Fy-Fres)A
1
= Yielded
Steel
1
2
2
3
3
Effects of Residual Stress
4
10
4
No Residual Stress
Notes: Maximum achieved load is therefore still P=AFy, but the load deflection curve is very different, stiffness is reduced.
10

## Slide 11
Euler Buckling

## Slide 12
Assumptions:
Column is pin-ended.
Column is initially perfectly straight.
Load is at centroid.
Material is linearly elastic (no yielding).
Member bends about principal axis (no twisting).
Plane sections remain Plane.
Small Deflection Theory.
Euler Buckling
Notes: A handout from any structural analysis text is worthwhile to show the derivation of the Euler Buckling Equation.

## Slide 13
e
s
E
D
P
Stable Equilibrium
Bifurcation Point
D
Euler Buckling
P
Notes: At the bifurcation point the member is mathematically indifferent between carrying additional load with no deflection or deflecting with no additional load strength. However, any actual member will have some perturbation (slight out of straightness or imperfect end conditions, etc.) which will make additional load impossible. It is also important to note that while the load deflection plots are typically shown as above, the theory is only valid for small deflections. Therefore the plot does not accurately describe actual column behavior.

## Slide 14
Dependent on Imin and L2.
Independent of Fy.
L
PE
Minor axis buckling
For similar unbraced length in each direction,
“minor axis” (Iy in a W-shape) will control strength.
14
Compression Theory
Major axis buckling
Euler Buckling
Notes: Euler Buckling plot of strength versus column length for a W-shape – note that each axis has a different strength – the lowest controls. Often a demonstration of buckling of an I-shape foam beam or slender ruler is effective. Students intuitively understand the controlling buckling axis-this plot provides a descriptive justification.
14

## Slide 15
PE =
divide by A, PE/A = , then with r2 = I/A,
PE/A = FE =
FE = Euler (elastic) buckling stress
L/r = slenderness ratio
Re-write in terms of stress:
Euler Buckling

## Slide 16
Buckling controlled by largest value of L/r.
Most slender section buckles first.
L/r
FE
Fy
Euler Buckling
Notes: For a given column length, the maximum value of L/r will occur when r is a minimum.
For a given column shape, the maximum value of L/r will occur when L is a maximum

## Slide 17
EULER ASSUMPTIONS
(ACTUAL BEHAVIOR)

## Slide 18
0 = initial mid-span deflection of column
Initial Crookedness/Out of Straight
P
P
M = PDo
Do
Do
Notes: First, what are the effects of a column that is not perfectly straight as expected by the Euler Buckling derivation? ASTM limits are noted to show that these are expected in an actual shape. The ASTM limits may change in the future, but the concept is the same regardless of the limiting value. An initial displacement 0, causes an initial moment along the length of the section, P0. This is greatest at the location of maximum deflection. Elastic theory then predicts the solid line in the plot to the right. Actual behavior, shown as the dashed line, is due to the additional effects of inelastic behavior. Yielding occurs from a combination of stresses due to moment and axial loads.

## Slide 19
D
P
Do= 0
Do
Initial Crookedness/Out of Straight

## Slide 20
D
P
Do= 0
Do
Elastic theory
20
Compression Theory
Initial Crookedness/Out of Straight

## Slide 21
D
P
Do= 0
Do
Elastic theory
21
Compression Theory
Actual Behavior
Initial Crookedness/Out of Straight
Notes: 21

## Slide 22
Buckling is not instantaneous.
ASTM limits of 0 = L/1000 or 0.25” in 20 feet
Typical values are 0 = L/1500 or 0.15” in 20 feet
Additional stresses due to bending of the column,
P/A  Mc/I.
Assuming elastic material theory (never yields),
P approaches PE.
Actually, some strength loss
small 0 => small loss in strength
large 0 => strength loss can be substantial
Initial Crookedness/Out of Straight
Notes: The first of these (along with the ductility of steel shapes) usually allows for some warning prior to a column failure. It also means that a column limited by “buckling” does not exhibit the classical instantaneaous buckling “failure” at a bifurcation point.

## Slide 23
D
P
e
L
D
Load Eccentricity
23
Compression Theory
D
P
Do= 0
Elastic theory
Notes: An initial load eccentricity, e, causes an initial moment along the length of the section, (Pe at the top). This is a similar effect to that of an initial out-of-straightness, namely the introduction of a moment in addition to the purely axial loading. Elastic theory then predicts the solid line in the plot to the right. Actual behavior, shown as the dashed line, is due to the additional effects of inelastic behavior. Yielding occurs from a combination of stresses due to moment and axial loads.
23

## Slide 24
D
P
e
L
D
Load Eccentricity
24
Compression Theory
D
P
Do= 0
Elastic theory
Actual Behavior
Notes: An initial load eccentricity, e, causes an initial moment along the length of the section, (Pe at the top). This is a similar effect to that of an initial out-of-straightness, namely the introduction of a moment in addition to the purely axial loading. Elastic theory then predicts the solid line in the plot to the right. Actual behavior, shown as the dashed line, is due to the additional effects of inelastic behavior. Yielding occurs from a combination of stresses due to moment and axial loads.
24

## Slide 25
If moment is “significant” section must be designed as a member subjected to combined loads.
Buckling is not instantaneous.
Additional stresses due to bending of the column,
P/A  Mc/I.
Assuming elastic material theory (never yields),
P approaches PE.
Actually, some strength loss
small e => small loss in strength
large e => strength loss can be substantial
Load Eccentricity
Notes: Note that “significant” moment is difficult to define. Most computer software design all members as beam-columns. The latter slides on columns address analysis methods where sections are analyzed as beam-columns for all cases. It is good to have students start thinking about the effects of moment on axial member design so they understand the concepts when beam-columns are introduced.

## Slide 26
Similar to pin-pin, with L’ = L/2.
Load Strength =
4 times as large.
EXAMPLE
KL
Set up equilibrium and solve similarly to Euler buckling derivation.
Determine a “K-factor.”
End Restraint (Fixed)
Notes: A derivation of the above example is provided in many structural analysis texts subsequent to the Euler Buckling strength derivation, and is found similarly. Charts of effective lengths and K-factors can be found in steel design texts and the AISC code as well.

## Slide 27
Length of equivalent pin ended column with similar elastic buckling load,
Effective Length = KL
End Restraint (Fixed)
Distance between points of inflection in the buckled shape.

## Slide 28
Handout on K-factors
EquivalentLength.pdf

## Slide 29
Fy
ET= Tangent Modulus
E
(Fy-Fres)
e
s
Test Results from an Axially Loaded Stub Column
Inelastic Material Effects
Notes: Inelastic material effects occur whenever axial stress in any portion of the cross section exceeds the first yield of the material (including residual stresses). This also compounds effects of out of straightness and load eccentricity, as the bending moment term introduced also results in longitudinal stresses.

## Slide 30
KL/r
Inelastic Material Effects
s
30
Compression Theory
Elastic Behavior
Notes: Inelastic action reduces column strength for lower values of KL/r. The maximum possible strength is the crushing limit, where all of the cross section attains Fy. Using tangent modulus theory, we can use a reduced modulus of elasticity, Et in the Euler Buckling equation. Et is obtained from a “Stub Column” (very short section in compression) test as shown on the previous page. Alternatively, one could assume that the entire cross section continues to have a material property, E, but that all yielded portions of the cross section are no longer effective, reducing I. In other words, ET = (Ie/I)E where Ie = I of non-yielded cross section. The end result is similar, as it is the combined stiffness parameter EI that controls the buckling strength.
30

## Slide 31
KL/r
s
31
Compression Theory
Fy-Fres
Fy
Inelastic
Elastic
Inelastic Material Effects
Notes: Inelastic action reduces column strength for lower values of KL/r. The maximum possible strength is the crushing limit, where all of the cross section attains Fy. Using tangent modulus theory, we can use a reduced modulus of elasticity, Et in the Euler Buckling equation. Et is obtained from a “Stub Column” (very short section in compression) test as shown on the previous page. Alternatively, one could assume that the entire cross section continues to have a material property, E, but that all yielded portions of the cross section are no longer effective, reducing I. In other words, ET = (Ie/I)E where Ie = I of non-yielded cross section. The end result is similar, as it is the combined stiffness parameter EI that controls the buckling strength.
31

## Slide 32
KL/r
s
32
Compression Theory
Fy-Fres
Fy
Inelastic
Elastic
Inelastic Material Effects
Notes: Inelastic action reduces column strength for lower values of KL/r. The maximum possible strength is the crushing limit, where all of the cross section attains Fy. Using tangent modulus theory, we can use a reduced modulus of elasticity, Et in the Euler Buckling equation. Et is obtained from a “Stub Column” (very short section in compression) test as shown on the previous page. Alternatively, one could assume that the entire cross section continues to have a material property, E, but that all yielded portions of the cross section are no longer effective, reducing I. In other words, ET = (Ie/I)E where Ie = I of non-yielded cross section. The end result is similar, as it is the combined stiffness parameter EI that controls the buckling strength.
32

## Slide 33
Elastic Buckling: ET = E
No yielding prior to buckling
Fe  Fy-Fres(max)
Fe = predicts buckling (EULER BUCKLING)
Two classes of buckling:
Inelastic Buckling:
Some yielding/loss of stiffness prior to buckling
Fe > Fy-Fres(max)
Fc - predicts buckling (INELASTIC BUCKLING)
Inelastic Material Effects

## Slide 34
Fy
KL/r
Experimental Data
Overall Column Strength
Notes: In general, the differences observed in testing of columns from Euler Buckling predicted capacities are as follows: Columns of low slenderness ratios are governed by inelastic buckling, and limited by crushing capacities. Columns of high slenderness ratios are limited by out of straightness effects. Columns of intermediate slenderness ratios see a combination of these effects.

## Slide 35
Fy
KL/r
Experimental Data
Inelastic Material effects
Including Residual Stresses
Out of Straightness
Overall Column Strength
35
Compression Theory
Notes: In general, the differences observed in testing of columns from Euler Buckling predicted capacities are as follows: Columns of low slenderness ratios are governed by inelastic buckling, and limited by crushing capacities. Columns of high slenderness ratios are limited by out of straightness effects. Columns of intermediate slenderness ratios see a combination of these effects.
35

## Slide 36
Major factors determining strength:
1) Slenderness (L/r).
2) End restraint (K factors).
3) Initial crookedness or load eccentricity.
4) Prior yielding or residual stresses.
Overall Column Strength
The latter 2 items are highly variable between specimens.

## Slide 37
LOCAL BUCKLING

## Slide 38
Local Buckling is related to Plate Buckling
Flange is restrained by the web at one edge.
Failure is localized at areas of high stress
(maximum moment) or imperfections.

## Slide 39
Local Buckling is related to Plate Buckling
Flange is restrained by the web at one edge.
Failure is localized at areas of high stress
(maximum moment) or imperfections.
39
Compression Theory
Notes: 39

## Slide 40
Local Buckling is related to Plate Buckling
Flange is restrained by the web at one edge.
40
Compression Theory
Failure is localized at areas of high stress
(maximum moment) or imperfections.
Notes: 40

## Slide 41
Local Buckling is related to Plate Buckling
Failure is localized at areas of high stress
(maximum moment) or imperfections.
Web is restrained by the flanges.

## Slide 42
Local Buckling is related to Plate Buckling
Failure is localized at areas of high stress
(maximum moment) or imperfections.
Web is restrained by the flanges.
42
Compression Theory
Notes: 42

## Slide 43
Local Buckling is related to Plate Buckling
Failure is localized at areas of high stress
(maximum moment) or imperfections.
Web is restrained by the flanges.
43
Compression Theory
Notes: 43

## Slide 44
FULL STRUCTURE BEHAVIOR
Notes: Column within a full structure will first be described as affecting the end conditions of a single column. Next the approach of full structure behavior including nominal forces (Direct Analysis Method) is introduced. This is covered in more detail in the Beam-Column design module.

## Slide 45
ALIGNMENT CHART
OR
DIRECT ANALYSIS METHODS
Notes: The instructor must decide how they wish to proceed here – both methods are presented and the instructor can select one or the other as their primary method.
The alignment chart is a more classical method, wherein structural interactions are included as end restraint on individual columns. Column design then proceeds as for an individual column but with a revised “K” factor. This is the more traditional approach and is covered in most text books.
Alternatively, Direct Analysis Methods are more common in international codes and are now introduced in AISC publications, with the likelihood of being the dominant design method in the future. This method is also easier to program for analysis and design in typical software packages. In this method, all members are designed as beam-columns with a “K” factor of 1.0. However, to account for structure interaction a series of notional loads are applied to the structure to develop moments in all “columns”, and these combined forces are calibrated to column capacities with K=1. As will be shown in beam-column modules these loads are based on rational principles, but require a slight “leap of faith” from the students to accept their values. If this method is chosen for instruction, it may be preferable to skip to beam-column design directly after addressing single column behavior and design.
Ideally both methods would be introduced, with an assignment comparing results for students to determine acceptability of the notional load values. Alignment chart procedures are often simpler for students to grasp conceptually while Direct Analysis methods easier for them to apply in a design.

## Slide 46
Does not redistribute restraining moments into girders/beams.
ALIGNMENT CHART
“Traditional Method”
Determine effective length, KL, for each column.
Basis for design similar to individual columns.
Notes: The alignment chart is a more classical method, wherein structural interactions are included as end restraint on individual columns. Column design then proceeds as for an individual column but with a revised “K” factor. This is the more traditional approach and is covered in most text books.

## Slide 47
DIRECT ANALYSIS METHOD
Analysis of entire structure interaction.
Include lateral “Notional” loads.
All members must be evaluated under combined axial and flexural load.
No K values required.
Reduce stiffness of structure.
Notes: Alternatively, Direct Analysis Methods are more common in international codes and are now included in AISC publications, with the likelihood of being the dominant design method in the future. This method is also easier to program for analysis and design in typical software packages. In this method, all members are designed as beam-columns with a “K” factor of 1.0. However, to account for structure interaction a series of notional loads are applied to the structure to develop moments in all “columns”, and these combined forces are calibrated to column capacities with K=1. As will be shown in beam-column modules these loads are based on rational principles, but require a slight “leap of faith” from the students to accept their values. If this method is chosen for instruction, it may be preferable to skip to beam-column design directly after addressing single column behavior and design.

## Slide 48
ALIGNMENT CHART METHOD
IS USED FOR THE FOLLOWING SLIDES
Notes: The instructor must decide how they wish to proceed here – both methods are presented and the instructor can select one or the other as their primary method.
The alignment chart is a more classical method, wherein structural interactions are included as end restraint on individual columns. Column design then proceeds as for an individual column but with a revised “K” factor. This is the more traditional approach and is covered in most text books.
Alternatively, Direct Analysis Methods are more common in international codes and are now included in AISC publications, with the likelihood of being the dominant design method in the future. This method is also easier to program for analysis and design in typical software packages. In this method, all members are designed as beam-columns with a “K” factor of 1.0. However, to account for structure interaction a series of notional loads are applied to the structure to develop moments in all “columns”, and these combined forces are calibrated to column capacities with K=1. As will be shown in beam-column modules these loads are based on rational principles, but require a slight “leap of faith” from the students to accept their values. If this method is chosen for instruction, it may be preferable to skip to beam-column design directly after addressing single column behavior and design.
Ideally both methods would be introduced, with an assignment comparing results for students to determine acceptability of the notional load values. Alignment chart procedures are often simpler for students to grasp conceptually while Direct Analysis methods easier for them to apply in a design.

## Slide 49
ALIGNMENT CHART
“Traditional Method”
Determine effective length, KL, for each column.
Basis for design similar to individual columns.
Does not redistribute restraining moments into girders/beams.
Notes: The alignment chart is a more classical method, wherein structural interactions are included as end restraint on individual columns. Column design then proceeds as for an individual column but with a revised “K” factor. This is the more traditional approach and is covered in most text books.

## Slide 50
K-FACTORS FOR END CONSTRAINTS
No Joint Translation Allowed – Sidesway Inhibited
0.5  K  1.0
Joint Translation Allowed – Sidesway Uninhibited
1.0  K  

## Slide 51
K-FACTORS FOR END CONSTRAINTS
Behavior of individual column unchanged
(Frame merely provides end conditions).
Two categories,
Braced Frames, 0.5  K  1.0
Sway Frames, K ≥ 1.0

## Slide 52
Floors do not translate relative to one another in-plane.
Typically, members are pin connected to save cost.
Sidesway Prevented

## Slide 53
Assume girder/beam infinitely rigid or flexible compared to columns to bound results.
K=0.7
K=0.5
K=1
K=0.7
Sidesway Prevented

## Slide 54
Shear Wall
Idealized
Equivalent
Sidesway Prevented
Notes: Note that even a brace or shear wall braces all attached nodes within the story if they are connected – and therefore act as bracing to linked columns.

## Slide 55
Shear Wall
Idealized
Equivalent
55
Compression Theory
Sidesway Prevented
Notes: Note that even a brace or shear wall braces all attached nodes within the story if they are connected – and therefore act as bracing to linked columns.
55

## Slide 56
Shear Wall
Idealized
Equivalent
56
Compression Theory
Sidesway Prevented
Notes: Note that even a brace or shear wall braces all attached nodes within the story if they are connected – and therefore act as bracing to linked columns.
56

## Slide 57
Typically, members are pin-connected to save cost (K = 1).
If members include fixity at connections,
Alignment Chart Method to account for rotational restraint (K < 1).
Typical design will assume K = 1 as a conservative upper bound (actual K ≈ 0.8 not much difference from K = 1 in design).
Sidesway Prevented

## Slide 58
Floors can translate relative to one another in-plane.
Enough members are fixed to provide stability.
Number of moment frames chosen to provide reasonable force distribution and redundancy.
Sway Frame

## Slide 59
Assume girder/beam infinitely rigid or flexible compared to columns to bound results.
K=2
K=1
K = ∞
K=2
Sway Frame

## Slide 60
Moment Frame
60
Compression Theory
Sway Frame
Notes: Note that even a single moment frame braces all attached nodes within the story if they are connected – though the rest of the structure is just “along for the ride”.
60

## Slide 61
61
Compression Theory
Moment Frame
Sway Frame
Notes: Note that even a single moment frame braces all attached nodes within the story if they are connected – though the rest of the structure is just “along for the ride”.
61

## Slide 62
62
Compression Theory
Moment Frame
Sway Frame
Notes: Note that even a single moment frame braces all attached nodes within the story if they are connected – though the rest of the structure is just “along for the ride”.
62

## Slide 63
Calculate “G” at the top and bottom of the column (GA and GB).
G is inversely proportional to the degree of rotational restraint at column ends.
I = moment of inertia of the members
L = length of the member between joints
Alignment Charts

## Slide 64
Alignment Charts
Separate Charts for Sidesway Inhibited and Uninhibited
Sidesway Inhibited
(Braced Frame)
Sidesway UnInhibited
(Sway Frame)
64
Compression Theory

## Slide 65
Alignment Charts
Separate Charts for Sidesway Inhibited and Uninhibited
Sidesway Inhibited
(Braced Frame)
Sidesway UnInhibited
(Sway Frame)
65
Compression Theory
Gtop
X
Gbottom
X
Gtop
X
Gbottom
X

## Slide 66
Alignment Charts
Separate Charts for Sidesway Inhibited and Uninhibited
Sidesway Inhibited
(Braced Frame)
Sidesway UnInhibited
(Sway Frame)
66
Compression Theory
Gtop
X
Gbottom
X
K
K
Gtop
X
Gbottom
X

## Slide 67
Use the IN-PLANE stiffness Ix if in major axis direction, Iy if in minor axis.
Girders/Beams are typically bending about Ix when column restraint is considered.
Only include members RIGIDLY ATTACHED (pin ended members are not included in G calculations).
If column base is “pinned” – theoretical G = ∞. AISC recommends use of 10.
If column base is “fixed” – theoretical G = 0. AISC recommends use of 1.
Alignment Charts

## Slide 68
ALIGNMENT CHART ASSUMPTIONS:
Behavior is purely elastic.
All members have constant cross section.
All joints are rigid.
Sidesway Inhibited (Braced) – single curvature bending of girders.
Sidesway Uninhibited (Sway) – reverse curvature bending of girders.
Stiffness parameter of all columns is equal.
Joint restraint is distributed to columns above and below the joint in proportion to EI/L of the columns.
All columns buckle simultaneously.
No significant axial compression force exists in the girders.
Alignment Charts

## Slide 69
Let’s evaluate the assumptions.
Alignment Charts

## Slide 70
ALIGNMENT CHART ASSUMPTIONS:
Behavior is purely elastic.
All members have constant cross section.
All joints are rigid.
Sidesway Inhibited (Braced) – single curvature bending of girders.
Sidesway Uninhibited (Sway) – reverse curvature bending of girders.
Stiffness parameter of all columns is equal.
Joint restraint is distributed to columns above and below the joint in proportion to EI/L of the columns.
All columns buckle simultaneously.
No significant axial compression force exists in the girders.
70
Compression Theory
Alignment Charts

## Slide 71
If the column behavior is inelastic,
Yielding decreases stiffness of the column.
Relative joint restraint of the girders increases.
G therefore decreases, as does K.
Decrease is typically small.
Conservative to ignore effects.
Can account for effects by using a
stiffness reduction factor (SRF), t, times G.
(SRF Table 4-13)
Alignment Charts

## Slide 72
ALIGNMENT CHART ASSUMPTIONS:
Behavior is purely elastic.
All members have constant cross section.
All joints are rigid.
Sidesway Inhibited (Braced) – single curvature bending of girders.
Sidesway Uninhibited (Sway) – reverse curvature bending of girders.
Stiffness parameter of all columns is equal.
Joint restraint is distributed to columns above and below the joint in proportion to EI/L of the columns.
All columns buckle simultaneously.
No significant axial compression force exists in the girders.
72
Compression Theory
Alignment Charts

## Slide 73
These conditions can be directly accounted for, but are generally avoided in design.
Partial restraint of connections and non-uniform members effectively change the rotational stiffness at the connections.
Only include members RIGIDLY ATTACHED (pin ended members are not included in G calculations).
Alignment Charts

## Slide 74
ALIGNMENT CHART ASSUMPTIONS:
Behavior is purely elastic.
All members have constant cross section.
All joints are rigid.
Sidesway Inhibited (Braced) – single curvature bending of girders.
Sidesway Uninhibited (Sway) – reverse curvature bending of girders.
Stiffness parameter of all columns is equal.
Joint restraint is distributed to columns above and below the joint in proportion to EI/L of the columns.
All columns buckle simultaneously.
No significant axial compression force exists in the girders.
74
Compression Theory
Alignment Charts

## Slide 75
Calculation of G accounts for rotational stiffness restraint at each joint based on assumed bending.
For other conditions include a correction factor “m” to account for actual rotational stiffness of the girder at the joint.
Alignment Charts

## Slide 76
Far end pinned
Bending Stiffness =
Bending Stiffness =
Bending Stiffness =
Sidesway Inhibited (Braced)
Assumption: single curvature bending of girder.
Far end fixed
Alignment Charts
m = (3EI/L)/(2EI/L) = 1.5
m = (4EI/L)/(2EI/L) = 2

## Slide 77
Far end pinned
Sidesway Uninhibited (Sway)
Assumption: reverse curvature bending of girder.
Far end fixed
Bending Stiffness =
Bending Stiffness =
Bending Stiffness =
Alignment Charts
m = (3EI/L)/(6EI/L) = 1/2
m = (4EI/L)/(6EI/L) = 2/3

## Slide 78
ALIGNMENT CHART ASSUMPTIONS:
Behavior is purely elastic.
All members have constant cross section.
All joints are rigid.
Sidesway Inhibited (Braced) – single curvature bending of girders.
Sidesway Uninhibited (Sway) – reverse curvature bending of girders.
Stiffness parameter of all columns is equal.
Joint restraint is distributed to columns above and below the joint in proportion to EI/L of the columns.
All columns buckle simultaneously.
No significant axial compression force exists in the girders.
78
Compression Theory
Alignment Charts

## Slide 79
Design typically checks each story independently, based on these assumptions.
In general, columns are chosen to be a similar size for more than one story. For each column section this results in sections with extra strength in upper floors, and close to their strength in lower floors.
Actual conditions can be directly accounted for, but are generally ignored in design.
Alignment Charts

## Slide 80
ALIGNMENT CHART ASSUMPTIONS:
Behavior is purely elastic.
All members have constant cross section.
All joints are rigid.
Sidesway Inhibited (Braced) – single curvature bending of girders.
Sidesway Uninhibited (Sway) – reverse curvature bending of girders.
Stiffness parameter of all columns is equal.
Joint restraint is distributed to columns above and below the joint in proportion to EI/L of the columns.
All columns buckle simultaneously.
No significant axial compression force exists in the girders.
80
Compression Theory
Alignment Charts

## Slide 81
This case will be addressed first, with the concept valid for general conditions as well.
In a story not all columns will be loaded to their full strength.
Some are ready to buckle, while others have additional strength.
An extreme case of this is a “leaner” column.
Alignment Charts

## Slide 82
“LEANER” COLUMNS

## Slide 83
Leaner Columns
For this structure note that the right columns are pinned at each connection, and provide no bending restraint.
Theoretically G at top and bottom is infinite.
83
Compression Theory
Moment Frame
Leaner Columns
Notes: 83

## Slide 84
Theoretically the column has an infinite KL.
Therefore, the strength should be zero.
For Leaner Columns:
G top= Infinity
G bottom= Infinity
Therefore K= Infinity
KL= Infinite
So the column has no strength according to the alignment chart
Leaner Columns

## Slide 85
Moment
Frame
Leaner Columns
Consider only applying a small load to the right columns
85
Compression Theory
Leaner Columns
Notes: 85

## Slide 86
Moment
Frame
Surely a small load could be applied without causing instability! (Due to connection to the rest of the structure)
Leaner Columns
Consider only applying a small load to the right columns
Leaner Columns

## Slide 87
PA
K = infinity
fPn = zero
PA
K < infinity
fPn > zero
Actual Condition
Chart
Provided that the moment frame is not loaded to its full strength, it can provide some lateral restraint to the leaner columns. This is indicated by the spring in the figure above.
Leaner Columns

## Slide 88
P
Note that the result of a vertical force trying to translate through displacement, D, is a lateral load of value PD/H applied to the system.
D
PD/H
H
PD/H
P
Leaner Columns

## Slide 89
leaner
1
2
3
4
P1
P2
P3
P4
ΣP = ΣPe
ΣP = P1+P2+P3+P4
ΣPe = P1e+P2e+P3e+P4e=P1e+P4e
In the elastic range, the “Sum of Forces” concept states that the total column capacities can be re-distributed
Leaner Columns

## Slide 90
leaner
1
2
3
4
P1
P2
P3
P4
If P2 = P2e
Reach failure even if
ΣP < ΣPe
However, the total load on a leaner column still must not exceed the non-sway strength.
Leaner Columns

## Slide 91
A system of columns for each story should be considered.
Actual design considers inelastic behavior of the sections, but the basic concept is the same.
The strength of the story is the load which would cause all columns to sway.
The strength of an individual column is the load which would cause it to buckle in the non-sway mode (K=1).
Leaner Columns

## Slide 92
EXAMPLE DEMONSTRATION –
SEE YURA VIDEOS

## Slide 93
Once the limit against lateral buckling and lateral restraint is reached, the entire story will exhibit sidesway buckling.
In general, each story is a system of columns which are loaded to varying degrees of their limiting strength.
Those with additional strength can provide lateral support to those which are at their sidesway buckling strength.
Alignment Chart

## Slide 94
Alignment Chart
ALIGNMENT CHART ASSUMPTIONS:
Behavior is purely elastic.
All members have constant cross section.
All joints are rigid.
Sidesway Inhibited (Braced) – single curvature bending of girders.
Sidesway Uninhibited (Sway) – reverse curvature bending of girders.
Stiffness parameter of all columns is equal.
Joint restraint is distributed to columns above and below the joint in proportion to EI/L of the columns.
All columns buckle simultaneously.
No significant axial compression force exists in the girders.
94
Compression Theory

## Slide 95
Axial load reduces bending stiffness of a section.
In girders, account for this with reduction factor on EI/L.
Alignment Chart

## Slide 96
If bending load dominates, consider the member a “girder” with reduced rotational stiffness at the joint (axial load reduction).
If axial load dominates, consider member a “column” with extra strength to prevent the story from buckling (sum of forces approach).
It is helpful to think in terms of members controlled by axial force or bending, rather than “girders” and “columns.”
Alignment Chart

## Slide 97
DIRECT ANALYSIS METHOD
IS USED FOR THE FOLLOWING SLIDES

## Slide 98
DIRECT ANALYSIS METHOD
Analysis of entire structure interaction.
Include lateral “Notional” loads.
No K values required.
Reduce stiffness of structure.
Notes: Alternatively, Direct Analysis Methods are more common in international codes and are included in AISC publications, with the likelihood of being the dominant design method in the future. This method is also easier to program for analysis and design in typical software packages. In this method, all members are designed as beam-columns with a “K” factor of 1.0. However, to account for structure interaction a series of notional loads are applied to the structure to develop moments in all “columns”, and these combined forces are calibrated to column capacities with K=1. As will be shown in beam-column modules these loads are based on rational principles, but require a slight “leap of faith” from the students to accept their values. If this method is chosen for instruction, it may be preferable to skip to beam-column design directly after addressing single column behavior and design.

## Slide 99
DIRECT ANALYSIS METHOD
Further evaluation of this method is included in the module on “Combined Forces.”